## Slide 1
CSE360: Computer Architecture
Section: 01
Mini-project Presentation

## Slide 2
Submitted by: (group – 09) | Submitted by: (group – 09)
Rihan Mahmud | 2020-2-60-123
Junnun Mohamed Karim | 2022-1-60-108
Md. Yousuf Hozaifa | 2022-1-60-162
Submitted To:
Dr. Md. Nawab Yousuf Ali Professor, Department of Computer Science & Engineering .
Our project is on-
Implement a Dynamic Branch Predictor Using a Perceptron Learning Algorithm in C

## Slide 3
Introduction

## Slide 4
  A wrong prediction wastes cycles as instructions from the wrong path are flushed.
  Correct predictions minimize delays, boosting overall throughput.
What is Branch Prediction?
Branch prediction is a key component in modern processors that enhances performance by guessing the outcome of conditional branch instructions before they are resolved.
Why does it matter?
What is a Perceptron?
A perceptron is a simple machine learning model inspired by biological neurons, designed to classify inputs based on a weighted sum of features and an activation threshold.
Why Perceptrons?
Perceptrons can learn patterns in historical data, making them ideal for identifying correlations between branch outcomes and branch history.

## Slide 5
Program Flow

## Slide 6
Initialization
This phase sets up the necessary resources, including logging, memory allocation, and global variables.
  Parse command-line arguments:
    Check for trace-file and --debug mode.
  Open the trace file for reading.
  Initialize the branch predictor:
    Initialize logging (if debug mode is enabled)
    Allocate memory for:
      Perceptron table.
      Global history.
      Path history.
    Reset statistics.

## Slide 7
Trace Processing
This phase processes the input trace file and performs branch predictions and training.
  Start reading the trace file line by line.
  For each branch instruction:
    Fetch the branch address and actual outcome.
    Compute the prediction using the perceptron predictor.
    Update statistics based on prediction accuracy.
    Train the perceptron if:
      The prediction was incorrect, OR
      The confidence is low.
  Update global and path history.

## Slide 8
Cleanup and Reporting
This phase handles memory cleanup and final statistics reporting.
  Print final statistics:
    Total predictions, mispredictions, accuracy, confidence, etc.
  Free allocated memory:
    Perceptron table.
    Global history.
    Path history.
  Close trace file and debug log (if enabled).

## Slide 9
Thank you
everyone!